Baling machine for recyclable waste

Product code MCD 05

Product details:

Exterior dimensions: 1610 x 940 x 1800 mm (Lx l x h)

Feeding table height: 1060 mm

Feeding table width: 600 mm

Weight: 675 kg

Bale diameter: max. 400 mm

Bale length: 600 mm

Bale weight: max. 30 kg

Bale density: 250-400 kg/m3

Baling capacity: 300 kg/h

Tying material: stretch foil of 23 μm

Foil spool diameter: 250 mm

Foil width: 580-595 mm

Grabbing speed: 0,36 m/s

Tri-phase engine: 3 kw.

Tying and bale ejection: semi-automatic

Bale diameter indicator: LED

Signal that indicates the maximum level of filling: acoustic.

Description:

- Mobile baler with manual feeding;

- Recommended for compacting following waste: large plastic bags, foam, fleece, cardboard, paper and paper padding, plastic foils, aluminum foils and bags, PP or PET strap, nonwoven;

- More robust alternative to MRD 01 model;

- Baling is achieved with the aid of 2 conveyor belts that are forming a round chamber for baling;

- Can be used continuously (no interruption = no dead time)

- Compacts the waste while being fed;

- Baling process can be interrupted at any moment, without allowing the material to re-expand (the material remains under permanent pressure, until the process is re-started);

- Provided with switch for the safety position;

- Can be installed in any place where work waste occurs;

- Requires a minimum operator effort;

- Also available in fully automated version of tying and evacuating the bale, provided

with bale diameter indicator as LCD display or with the possibility of presetting the

bale diameter.